## Slide 1: Digital Electronics and Systems Course Code: EEE 471 ENGR. FABUNMI T. E.

## Slide 2
Course Outline
Number Systems and Codes
Logic Gate Simplification of Logic expressions using Boolean Algebra.
Simplification of Logic expressions using Karnaugh Method
Design combinational circuit
Flip-Flops
Application of Flip-Flops in the design of counters, registers and timers

## Slide 3
Switching and Waves shipping circuit
Generation of non-sinusoidal signal (multi vibrators)
Introduction to ADC and DAC
Design of Logic Gates (Diode, DTL, TTL, ECL, CMOS families etc)
Memory devices
Latches
Decoders and encoders

## Slide 4
Multiplexer circuits
Computer-aided design of Modular Systems
Synchronous and asynchronous operations
Analysis and synthesis of sequential switching circuits, Registers
Introduction to instruction format: OPCODE OPERAND

## Slide 5
Binary representation: bits, nibbles, bytes: character representation: numeric, non-numeric, alphanumeric, EBCDIC, BCID, ASCII, and ANSII
Fundamental building blocks (logic gates, flip-flops, counters, registers, PLA/PAL)
Design of combinatorial circuits with emphasis on application

## Slide 6
Design of sequential circuits, synchronous and asynchronous
Design of simple CPU, peripheral devices (I/O), memory/storage devices
Stored-program concept
Introduction to programming of microcontrollers

## Slide 7
Number Systems and Codes

## Slide 8
This is a system of naming or representing numbers.
The study of number systems is important from the viewpoint of understanding how data are represented before they can be processed by any digital system including a digital computer. The different number systems commonly used to represent data will be discussed.
There are two basic ways of representing the numerical values of the various physical quantities with which we constantly deal in our day-to-day lives. These are analogue and digital systems
Number Systems and Codes

## Slide 9
Types Of Number Systems
Decimal Number System
Binary Number System
Octal Number System
Hexadecimal Number System

## Slide 10
Decimal Number System
The decimal number system is a radix-10 number system and therefore has 10 different digits or
symbols. These are 0, 1, 2, 3, 4, 5, 6, 7, 8 and 9. All higher numbers after ‘9’ are represented in terms
of these 10 digits only.
Binary Number System
The binary number system is a radix-2 number system with ‘0’ and ‘1’ as the two independent digits.
All larger binary numbers are represented in terms of ‘0’ and ‘1’. Each digit in binary is a 0 or a 1 and is called a bit, which is an abbreviation of binary digit.

## Slide 11
Octal Number System
The octal number system has a radix of 8 and therefore has eight distinct digits. The independent digits
are 0, 1, 2, 3, 4, 5, 6 and 7.
Hexadecimal Number System
The hexadecimal number system is a radix-16 number system and its 16 basic digits are 0, 1, 2, 3,
4, 5, 6, 7, 8, 9, A, B, C, D, E and F. The place values or weights of different digits in a mixed
hexadecimal number are 160, 161, 162 and so on (for the integer part) and 16−1, 16−2, 16−3 and so on
(for the fractional part).

## Slide 13
Binary Codes
The binary coding system, called the straight binary code as becomes very cumbersome to handle when used to represent larger decimal numbers. To overcome this shortcoming, and also to perform many other special functions, several binary codes have evolved over the years. Some of the better-known binary codes, including those used efficiently to represent numeric and alphanumeric data, and the codes used to perform special functions, such as detection and correction of errors

## Slide 14
Types of Binary Codes
Binary Coded Decimal
Excess-3 Code
Gray Code
Alphanumeric Codes
Seven-segment Display Code
Error Detection and Correction Codes

## Slide 15
Assignment
Discus the various types of binary codes
An SD card can store 200megabytes of digital data. Given that mega = 220 , how many bits of data can the SD card hold?

## Slide 16
LOGIC GATES
Logic gates are electronic circuits that can be used to implement the most elementary logic expressions,
also known as Boolean expressions. The logic gate is the most basic building block of combinational
logic. There are three basic logic gates, namely the OR gate, the AND gate and the NOT gate. Other
logic gates that are derived from these basic gates are the NAND gate, the NOR gate, the EXCLUSIVEOR
gate and the EXCLUSIVE-NOR gate.

## Slide 18
Karnaugh Map
A Karnaugh map is a graphical representation of the logic system.
Construction of a Karnaugh Map
An n-variable Karnaugh map has 2n squares, and each possible input is allotted a square. In the case of a minterm Karnaugh map, ‘1’ is placed in all those squares for which the output is ‘1’, and ‘0’ is placed in all those squares for which the output is ‘0’.

## Slide 19
Having drawn the Karnaugh map, the next step is to form groups of 1s as per the following guidelines:
1. Each square containing a ‘1’ must be considered at least once, although it can be considered as often as desired.
2. The objective should be to account for all the marked squares in the minimum number of groups.
3. The number of squares in a group must always be a power of 2, i.e. groups can have 1, 2, 4 8, 16, squares.
4. Each group should be as large as possible, which means that a square should not be accounted for by itself if it can be accounted for by a group of two squares; a group of two squares should not be made if the involved squares can be included in a group of four squares and so on.
5. ‘Don’t care’ entries can be used in accounting for all of 1-squares to make optimum groups. They are marked ‘X’ in the corresponding squares. It is, however, not necessary to account for all ‘don’t care’ entries. Only such entries that can be used to advantage should be used.